## Slide 1: Musculoskeletal Model of Fingers to Enable Design of Prosthetic Gloves
By Shashank Swaminathan

## Slide 2: Overall Proposal
Premise:
  By thoroughly understanding the relationship between muscle actuation and grasping characteristics of the hand, it is possible to improve design and control of prosthetic assist technologies.
Question: Can mathematical model based analysis be used to investigate the musculoskeletal dynamics of the hand?

## Slide 3: Design Question
θ
Stiffness
Load
θ
Stiffness
Load
Muscle Activation Percentages
Muscle Activation Percentages
?
Physiology
Brace Operation

## Slide 4: Functional Unit Component Model
Scope of Project
Posterior Muscle
Anterior Muscle
Bone 1
Bone 2
θdesired
FA
FP
τ, dτ/dθ
Goal

## Slide 5: Design of the Muscle-Joint Component
Anterior Muscle
Posterior Muscle
Lower Bone
Upper Bone
Muscle Threading Points
Restraining Revolute Joint

## Slide 6: Bone-Muscle Joint Model Implementation
Above is the model of a single bone-muscle-joint system
Modelica was used to represent the physical equations
SystemModeler was the simulation tool
  The MultiBody library in SystemModeler was used for rigid-body analysis

## Slide 7: Bone-Muscle Joint Model Implementation
Above is the muscle model

## Slide 8: Bone-Muscle Joint Model Implementation
Above is the restraining revolute joint component

## Slide 9: Experiment Procedure
Figure 1
Figure 2
Set value for FP
Set values for θ and τ
Ramp values for FA, and simulate
Determine value for FA (figure 1)
Set determined value for FA
Perturb value of θ
Simulate and graph τ vs. θ
Determine from slope dτ/dθ (figure 2)
This process is automated using Mathematica

## Slide 10
Muscle Activation Mapping Results
Different surfaces represent different load values

## Slide 11
Validation of Approach
Muscle actuation for desired theta and stiffness
Desired Stiffness: 2.19318 Nm/rad Achieved Stiffness: 2.19228
Desired Angle: 1.1 rad Achieved Angle: 1.1 rad

## Slide 13
Conclusion
I successfully mapped the relationship between the angle of contraction, the load, the effective stiffness, and the muscle actuation values.
I can now use this mapping to control the joint movement to achieve the desired output.
From the results the primary question of the project is answered:
  Mathematical model based analysis be used to describe the musculoskeletal dynamics of the hand

## Slide 14: Further Work
I will increase the scope of the model from the functional unit model to a full-scale hand model
After completing this, I can then begin to integrate this understanding into building a prototype